## Slide 1
ICMTC SATELLITE CHALLENGE · SATC-6 · TASK II
Coarse Sun Sensor
Critical Design Review
Team Name: AAST NOVA
Roles: Electronics & Firmware · Software & GUI · Integration & Test
2026

## Slide 2
R O A D M A P
Agenda
01
Mission & Requirements
Sensor role, mandatory minimums, and our competition strategy
02
PCB Design
Board layout, routing, and component placement decisions
03
Components
Key hardware selections across the signal chain
04
End-to-End Architecture
Full system view from photodiodes to ground display
Firmware
ESP32 firmware architecture and control logic
GUI
Python/PyQt5 operator interface and telemetry display
Future Trends
Calibration, ML-based enhancements, and next steps
Coarse Sun Sensor CDR
05
06
07

## Slide 3
MISSION CONTEXT
Role of a Coarse Sun Sensor
Without knowing where the sun is, a satellite can lose power, overheat, or lose control entirely.
1. Attitude Determination: The primary mission is to tell the spacecraft where the Sun is relative to its body.
2.Attitude control: Orienting the satellite so it points to the desired aim. For solar panels, antennas, pointing cameras
3. Safe Mode Recovery: the satellite's last-resort failsafe when other systems fail
4.Protecting Sensitive Instruments: Some cameras, telescopes, and scientific instruments can be damaged by direct sunlight or high temperature.
±80° FIELD OF VIEW
(mandatory minimum: ±60°)
Coarse Sun Sensor CDR

## Slide 4
DESIGN TARGETS
Requirements & Competition Strategy
Our strategy targets bonus-scoring performance, not just minimum compliance. Every headline spec is designed with margin above the mandatory floor.
Parameter | Mandatory Minimum | Our Design Target | Margin
Field of View | ±60° | ±80° | +33%
Update Rate | 5 Hz | 10 Hz | 2×
Sun Channels | 1 axis | 4 photodiodes (2-axis) | Full coverage
Thermal Monitoring | Not required | Dual DS18B20 sensors | Added robustness
Coarse Sun Sensor CDR

## Slide 5
System Design
Components
Coarse Sun Sensor CDR
1. ESP32-S (Microcontroller)
  Controls the entire sun sensor system
  Reads ADC data via I²C
  Polls temperature sensors
  Executes sun-detection algorithm
  Controls status LEDs
  Sends telemetry to the GUI
Advantages
  Dual-core processor for fast data processing
  Built-in Wi-Fi and Bluetooth
  Large number of GPIO pins
  Low cost.
  Extensive Arduino library support

## Slide 6
System Design
Components
Coarse Sun Sensor CDR
2. ADS1115 (16-bit ADC)
  Converts amplified photodiode voltages into digital values
  Transfers data to the ESP32 via I²C
Advantages
  High 16-bit resolution for accurate measurements
  Built-in Programmable Gain Amplifier (PGA)
  Simple I²C interface (SDA & SCL)
  Multiple selectable I²C addresses
  Low-noise performance

## Slide 7
System Design
Components
Coarse Sun Sensor CDR
3. LM358P (Dual Operational Amplifier)
  Implements the Transimpedance Amplifier (TIA)
  Converts photodiode current into measurable voltage
Advantages
  Two op-amps in one package
  Operates from a single power supply
  Low power consumption
  Low cost
  Suitable for low-speed sensor applications

## Slide 8
System Design
Components
Coarse Sun Sensor CDR
4. DS18B20 (Digital Temperature Sensor)
  Measures temperature
  Provides thermal monitoring and calibration data
Advantages
  Digital output (no analog conditioning required)
  High accuracy (±0.5°C)
  OneWire interface reduces wiring
  Unique factory-programmed ID for each sensor
  Low power and compact size

## Slide 9
System Design
Components
Coarse Sun Sensor CDR
5. BPW34 (Silicon Photodiode)
  Detects sunlight
  Converts incident light into photocurrent
  Provides four sensing channels for angle estimation
Advantages
  Wide spectral response (Visible (430 to 680 nm)+ Near-IR (1100 nm))
  Fast response time
  Low cost
  Easy to integrate into sensor arrays
  Stable and well-characterized performance

## Slide 10
System Design
Coarse Sun Sensor CDR
Cross-shaped wall
Separates the four photodiodes to limit each sensor's field of view.
Reduces stray light and optical crosstalk.
Improves angle estimation accuracy.
Enables the required field of view (up to ±80° depending on the geometry).
The equation used is θ=tan−1(d/h​)
Dimensions 50*50mm
Wall thickness 2mm
Wall height 8mm
Quadrant size 24x24

## Slide 11
SYSTEM DESIGN
End-to-End System Architecture
4× BPW34
Photodiodes
Silicon sun-angle sensing
TIA Stage
LM358P
Inverting transimpedance amp
ADS1115
16-bit ADC
I²C, GPIO21/22 · 0x48
ESP32-S
MCU
Acquisition & control
Python GUI
(Ground)
Real-time visualization
2× DS18B20 Temp Sensors + Status LEDs (Green / Yellow)
Signal flows left to right: analog sun-angle sensing, conditioning, digitization, onboard processing, then wireless/serial reporting to the ground GUI.
Coarse Sun Sensor CDR

## Slide 12
HARDWARE · ANALOG FRONT END
Photodiode Array & Signal Conditioning
4× BPW34 Silicon Photodiodes
Arranged for multi-axis sun-angle discrimination; wide spectral response in the visible/near-IR band matches solar irradiance.
Inverting Transimpedance Stage
Each photodiode feeds a dedicated inverting TIA, converting photocurrent to a clean, amplified voltage.
Dual LM358P Op-Amps, Feedback resistor + 12 pF Compensation
Low-power dual op-amps set gain via 100 kΩ feedback resistors, with a 12 pF capacitor in parallel across each feedback resistor to limit bandwidth and suppress high-frequency noise/oscillation — balancing sensitivity against noise and saturation margin.
PER-CHANNEL SIGNAL CHAIN
Photodiode
(BPW34)
Inverting TIA
(LM358P)
Feedback R + C
Buffered
Output Voltage
Gain per channel is fixed by the 100 kΩ feedback resistor, with the parallel 12 pF capacitor stabilizing the response — giving predictable, repeatable calibration across all four sensing channels.
Coarse Sun Sensor CDR

## Slide 13
HARDWARE · HOUSEKEEPING
Thermal Monitoring & Status Indication
2× DS18B20 Digital Sensors
OneWire bus on GPIO4 and GPIO5 with a 4.7 kΩ pull-up resistor. Dual placement tracks thermal gradients across the sensor board — not required by the competition, but added for robustness.
White Status LED
Illuminates during sun presence.
Red Status LED
Illuminates when the temperature is greater than 30, giving an at-a-glance operational check without the GUI.
Resistors: 220 Ω current-limiting on each status LED · 4.7 kΩ pull-up on the OneWire temperature bus.
Coarse Sun Sensor CDR

## Slide 14
Breadboard connections

## Slide 15
PCB Design
(1)
Two-layer PCB
(2)

## Slide 16
  Grouping the analog signal path (photodiodes ,op-amps and ADC) close together to keep those traces short to reduce the noise since the generated signal is very weak.
  Rounded corners to improve signal integrity since Sudden changes in trace geometry can create impedance discontinuities, which may introduce signal reflections and degrade performance.
PCB Design

## Slide 17
PCB Connections

## Slide 21
SOFTWARE · GROUND SEGMENT
Python Ground Control GUI
The ground-side GUI gives the operator a live window into subsystem health and sun-tracking performance during test and demonstration.
SUN DETECTED — Node ID 01
Coarse Sun Sensor CDR

## Slide 22
Coarse Sun Sensor CDR
Improve angular accuracy through multi-point calibration.
Increase telemetry update rate above 10HZ.
Replace ESP32 with STM32.
Implement automatic self-calibration and temperature compensation.
Develop a more advanced GUI with 3D visualization and data export.
Future trends
Successfully developed a functional Coarse Sun Sensor for satellite attitude determination.
Achieved real-time Sun angle estimation, Sun detection, temperature monitoring, and telemetry transmission.
Met the main competition requirements, including ≥5 Hz update rate and ≥±80° Field of View.
Delivered a reliable, low-cost, and scalable system suitable for CubeSat missions, with potential for future improvements.
Conclusion

## Slide 23
Thank you — questions welcome.
Coarse Sun Sensor CDR